## Slide 1: Traffic Sign Detection
Computer Vision – Project 1 – MIEIC – 13/14
Carlos Miguel Correia da Costa – 200903044 – Carlos.costa@fe.up.pt

## Slide 2: 1. Applications
Fig 1.2 - Autonomous vehicles
Fig. 1.1 - Driver assistance systems

## Slide 3: 2. Implementation main algorithms
Scene acquisition (image, video, camera)
Image preprocessing
Signal color segmentation
Text color segmentation
Traffic sign recognition

## Slide 4: 2.1. Image preprocessing
Bilateral filtering
Fig. 2.1a – Effect of the bilateral filter in removing noise

## Slide 5: 2.1. Image preprocessing
Contrast limited adaptive histogram equalization (CLAHE)
Fig. 2.1b – Effect of the CLAHE in increasing contrast

## Slide 6: 2.1. Image preprocessing
Contrast and brightness correction
Fig. 2.1c – Correction of contrast and removal of noise

## Slide 7: 2.2. Signal color segmentation
Signal segmentation in HSV color space using the red borders
Usage of opening morphological operation to remove small blobs
Fig. 2.2a – Identification of possible traffic sign positions using color segmentation

## Slide 8: 2.2. Signal color segmentation
Identification of signals circles using HoughCircles transform
Detection of signals borders with OpenCV fitEllipse
Fig. 2.2b – Usage of HoughCircles transform and ellipse extraction to segment the signals from the image

## Slide 9: 2.3. Text color segmentation
Extraction of each signal from the image, removing the background
Segment text only inside signs ellipsis
Usage of erosion operation to thin the text and improve recognition
Fig. 2.3a – Text extraction using color segmentation
Fig. 2.3b – Application of the erosion operator

## Slide 10: 2.4. Traffic sign recognition
Application of template matching or feature detection to identify the numbers inside the traffic signs ellipsis
Fig. 2.4a – Number recognition using GoodFeaturesToTrackDetector, SiftDescriptorExtractor and FlannBasedMatcher

## Slide 11: 2.4. Traffic sign recognition
Feature detection results for signals with good segmentation and positioning
Fig. 2.4b – Good matches between feature points

## Slide 12: 2.4. Traffic sign recognition
Feature detection results for signals with good segmentation and some perspective distortion
Fig. 2.4c – Good matches between feature points

## Slide 13: 2.4. Traffic sign recognition
Feature detection results for signals with suboptimal segmentation (on purpose), and how the feature points adapted
Fig. 2.4d – Good matches between feature points

## Slide 14: Questions?